## Slide 1: Device Drivers for Embedded Internet of Things (IoTs) Platforms

## Slide 2: Content
Device Driver Overview
Serial Communication Device Driver
  Universal Asynchronous Receiver/Transmitter (UART)
  Serial Peripheral Interface (SPI)
  Inter-Integrated Circuit (I2C)
Summary

## Slide 3: What is Device Driver?
Device driver is a particular software application that is designed to enable interaction with hardware devices.
Device drivers are operating system-specific and hardware-dependent.
For embedded platforms running OS, device drivers are considered as part of firmware.
Firmware is the software which executes on the embedded system's CPU (written in assembler and C), was complied and the binary burned onto an EPROM.

## Slide 4: Why Do We Need Device Driver?
Provide uniform APIs to access hardware.
Custom platforms
  Contain many peripheral devices and kernel supported CPU
    Get kernel to boot on the board
    Device drivers to allow applications to access peripheral devices

## Slide 5: Device Driver Models
Device drivers, over the years, have become very complex
  Drivers are separated into classes
    Serial, network, audio, video, touch panel, etc.
  Layer approach is used
    To support a new device, a layer is modified instead of rewriting the entire driver
    Processing functions required for a given class often do not require modification

## Slide 6: Device Driver Architecture
Device Drivers
Interrupt Service Threads
Interrrupt Service Routines
HAL
Kernel
User Mode
Kernel Mode

## Slide 7: Serial Communication using UART
The most popular connection in hardware devices
What is the difference between UART, RS232 and RS485?

## Slide 8: UART Device Driver on Android Things
UART stands for Universal Asynchronous Receiver Transmitter
It is universal because both the data transfer speed and data byte format are configurable.
It is asynchronous in that there are no clock signals present to synchronize the data transfer between the two devices
UART data transfer is full-duplex, meaning data can be sent and received at the same time

## Slide 9: UART Implementation
https://github.com/androidthings/sample-uartloopback
Adding the required permission
Managing the connection
<uses-permission android:name="com.google.android.things.permission.USE_PERIPHERAL_IO" />
PeripheralManager manager = PeripheralManager.getInstance(); List<String> deviceList = manager.getUartDeviceList(); if (deviceList.isEmpty()) { Log.i(TAG, "No UART port available on this device."); } else { Log.i(TAG, "List of available devices: " + deviceList); }

## Slide 10: UART Implementation
Open an UART Port
Close an UART Port
try { PeripheralManager manager = PeripheralManager.getInstance(); mDevice = manager.openUartDevice(UART_DEVICE_NAME); } catch (IOException e) { Log.w(TAG, "Unable to access UART device", e); }
@Override protected void onDestroy() { super.onDestroy(); if (mDevice != null) { try { mDevice.close(); mDevice = null; } catch (IOException e) { Log.w(TAG, "Unable to close UART device", e); } } }
private UartDevice mDevice;

## Slide 11: UART Implementation
Configure the frame format
Baudrate: Communication speed in baud. In computer, it is equivalent to bits per second (bps)
public void configureUartFrame(UartDevice uart) throws IOException { // Configure the UART port uart.setBaudrate(115200); uart.setDataSize(8); uart.setParity(UartDevice.PARITY_NONE); uart.setStopBits(1); }

## Slide 12: UART Implementation
Send a message
Receive a message
public void writeUartData(UartDevice uart) throws IOException { byte[] buffer = {...}; int count = uart.write(buffer, buffer.length); Log.d(TAG, "Wrote " + count + " bytes to peripheral"); }
private UartDeviceCallback mUartCallback = new UartDeviceCallback() { @Override public boolean onUartDeviceDataAvailable(UartDevice uart) { // Read available data from the UART device try { readUartBuffer(uart); } catch (IOException e) { Log.w(TAG, "Unable to access UART device", e); } return true; } @Override public void onUartDeviceError(UartDevice uart, int error) { Log.w(TAG, uart + ": Error event " + error); } };
public void readUartBuffer(UartDevice uart) throws IOException { // Maximum amount of data to read at one time final int maxCount = ...; byte[] buffer = new byte[maxCount]; int count; while ((count = uart.read(buffer, buffer.length)) > 0) { Log.d(TAG, "Read " + count + " bytes from peripheral"); } }

## Slide 13: Wireless Modules using UART Interface
AT command (AT stands for attention)
Bluetooth
XBee
GSM/GPRS
LORA
(SX1728)
Wifi
(ESP8266)

## Slide 14: Hyper Terminal https://www.dropbox.com/s/7xuwege5pjv6fis/Terminal.exe?dl=0
1. Set Baudrate
3. Select COM Port
4. Click Connect
5. Send a testing command (AT)

## Slide 15: Example AT Commands for GSM/GPRS
Send a SMS message to a phone:
  AT+CMGF=1
  AT+CSCS="GSM"
  AT+CMGS="84906362340"
  Send text message
  0x1A
Send a GET request:
  AT+SAPBR=1,1
  AT+HTTPINIT
  AT+HTTPPARA="CID",1
  AT+HTTPPARA="URL","http://www.iforce2d.net/test.php"
  AT+HTTPACTION=0
  AT+HTTPREAD
  AT+HTTPTERM
Note: Every AT command ends with carry return
  \r\n
  0x0d 0x0a

## Slide 16: Serial Communication using SPI
Serial Peripheral Interface (SPI) is an interface bus commonly used to send data between microcontrollers and small peripherals such as shift registers, sensors, and SD cards
Separate clock (SCK), data lines (MISO, MOSI) and chip select (CS) are used.
Synchronous protocol

## Slide 17: Asynchronous vs Synchronous Protocol
Asynchronous (UART):
  There is no CLOCK
  Clock drift issue  low speed
Synchronous (SPI):
  There is a CLOCK line
  High speed

## Slide 18: SPI Protocol
Clock is generated by the master

## Slide 19: SPI Device Driver on Android Things
Serial Peripheral Interface (SPI) devices are typically found where fast data transfer rates are required (e.g. external non-volatile memory and graphical displays)
Clock speeds are typically in the 16MHz to 25MHz range.

## Slide 20: Implement SPI
Adding the required permission
Managing the device connection
<uses-permission android:name="com.google.android.things.permission.USE_PERIPHERAL_IO" />
PeripheralManager manager = PeripheralManager.getInstance(); List<String> deviceList = manager.getSpiBusList(); if (deviceList.isEmpty()) { Log.i(TAG, "No SPI bus available on this device."); } else { Log.i(TAG, "List of available devices: " + deviceList); }

## Slide 21: Implementation SPI
Open SPI Port
Close SPI Port
try { PeripheralManager manager = PeripheralManager.getInstance(); mDevice = manager.openSpiDevice(SPI_DEVICE_NAME); } catch (IOException e) { Log.w(TAG, "Unable to access SPI device", e); }
@Override protected void onDestroy() { super.onDestroy(); if (mDevice != null) { try { mDevice.close(); mDevice = null; } catch (IOException e) { Log.w(TAG, "Unable to close SPI device", e); } } }

## Slide 22: Implement SPI
Configure SPI connection
  MODE0: Clock signal idles low, data is transferred on the leading clock edge
  MODE1: Clock signal idles low, data is transferred on the trailing clock edge
  MODE2: Clock signal idles high, data is transferred on the leading clock edge
  MODE3: Clock signal idles high, data is transferred on the trailing clock edge
public void configureSpiDevice(SpiDevice device) throws IOException { // Low clock, leading edge transfer device.setMode(SpiDevice.MODE0); // 16MHz, 8BPW, MSB first device.setFrequency(16000000); device.setBitsPerWord(8); device.setBitJustification(SpiDevice.BIT_JUSTIFICATION_MSB_FIRST); }

## Slide 23: Implement SPI
Transferring and Receiving Data
If 2 bytes are sent and 2 bytes will be received, how many bytes for the buffer (the second parameter in sendCommand function)???
public void sendCommand(SpiDevice device, byte[] buffer) throws IOException { // Shift data out to slave device.write(buffer, buffer.length); // Read the response byte[] response = new byte[32]; device.read(response, response.length); ... }

## Slide 24: Serial Communication using I2C
Inter-integrated Circuit (I2C) Protocol is a protocol intended to allow multiple “slave” digital integrated circuits (“chips”) to communicate with one or more “master” chips.
Like the Serial Peripheral Interface (SPI), it is only intended for short distance communications within a single device.
Like Asynchronous Serial Interfaces (such as RS-232 or UARTs), it only requires two signal wires to exchange information.

## Slide 25: I2C vs SPI
Number of pins  Difficult in tight PCB layout
SPI only allows one master on the bus
SPI is good for high data rate full-duplex
Only two pins, like asynchronous serial, but can support up to 128 slave devices
Support a multi-master system
Data rates is at 100kHz or 400kHz

## Slide 26: I2C Protocol
Master sends START condition and controls the clock (SCL)
Master sends a unique 7-bit slave address
Master sends Read/Write bit: 0 write to slave, 1: read from slave
Slave which address is matched send ACK bit
Data (8bit) is transfered

## Slide 27: Implement I2C
I2C is a synchronous serial interface. The device in control of triggering the clock signal is known as the master. All other connected peripherals are known as slaves. Each device is connected to the same set of data signals to form a bus.
https://developer.android.com/things/sdk/pio/i2c

## Slide 28: Summary
UART = Universal Asynchronous Receiver / Transmitter
SPI = Serial Peripheral Interface
I2C = Inter-Integrated Circuit

## Slide 29: Serial Communications Methods
Name | Description | Function
I2C | Inter-Integrated Circuit | Half duplex, serial data transmission used for short-distance between boards, modules and peripherals. Uses 2 pins.
SPI | Serial Peripheral Interface bus | Full-duplex, serial data transmission used for short-distance between devices. Uses 4 pins.
UART | Universal Asynchronous Receiver-Transmitter | Full-duplex, Asynchronous, serial data transmission between devices. Uses 2 pins.

## Slide 30: Conclusion
UART - simple; not high speed; no clock needed; limited to one device connected to the Pi.
I2C - faster than UART, but not as fast as SPI; easier to chain many devices; Pi drives the clock so no sync issues.
SPI - fastest of the three; Pi drives the clock so no sync issues; practical limit to number of devices on the Pi.